## Slide 1: Design Project
Scope of Project
  Define Problem
  List Objectives
Management of Project
  Partition of Work
  Timeline
Engineering
  Design / Calculation and Simulation
  Selection / Cost Analysis
  Implementation
  Diagnosis
Report

## Slide 2: Multistage Amplifier Design
High gain
High input impedance
Low output impedance
Large signal swing
Large bandwidth
Opportunity for DESIGN!

## Slide 3: Design Goals
Av > 300
Peak-to-peak output voltage without distortion > 4 V
Low frequency -3dB point < 50 Hz
High frequency -3dB point > 15 kHz
Input resistance at 10 kHz > 200 kW
Output impedance < 200 W

## Slide 4: Rules
VCC < 10 V; VDD > -10 V
No operational amplifier
Any number and combinations of BJT, MOSFET or JFET
10-kW load resistor attached

## Slide 5: Procedures
Design from last stage backward.
Run simulation.
Find ac frequency response.
Revise the circuit.
Run simulation again.
Get sufficient gain and bandwidth.
Increase the input signal.
Adjust biases to eliminate clipping.

## Slide 6: Considerations
High Input Impedance
  JFET or MOSFET
High Gain
  BJT in CE configuration
Low Output Impedance
  BJT in CC configuration
AC Coupling
  Isolate bias conditions

## Slide 7: Example

## Slide 8: Functional Blocks
JFET or MOSFET Input Stage
  High impedance
BJT CE Gain Stage
  High voltage gain
BJT CC Output Stage
  Low output impedance
Coupling Capacitors
  DC bias conditions isolated

## Slide 9: Optimization
Bias Conditions
  Waveform clipping
  One stage at a time
Low Frequency Cut Off
  Capacitors
High Frequency Cut Off
  Gain related

## Slide 10: Self Oscillation
Oscillation
  High gain
  Positive feedback via stray inductance
  Waveform blur with high f oscillation
Solutions:
  Connect a bypass capacitor across power supply and ground on the prototype board.
  Connect a small capacitor between collector and base.

## Slide 11: A Real Challenge
Build a dc coupled multi-stage amplifier.
Level shifter or dual power supply

## Slide 12: DC Coupled Amplifier
No coupling capacitors
No bias resistors
Next challenge – bypass capacitors

## Slide 13: More Ambitious Endeavor
Design your own operational amplifier!