## Slide 1: Unit 4. Current-voltage characteristics of ideal MOSFETs Design and process parameters
  Enhancement mode
  n-channel MOSFETs
  Required bias voltages
  for constant output current
  Operation in saturation mode
  Family of output characteristics
  Transfer characteristic
  p-channel MOSFETs
  Design and process parameters
  MOSFET symbols

## Slide 2: Major integrated circuit technologies
Bipolar CMOS
npn + pnp nMOS + pMOS
High frequencies: Lower dissipated power
Low frequencies: Lower noise Lower dissipated power
Lower DC offset voltage
(better device matching)
Lower input current
Which one is better for integrated circuits (OpAmp)? It depends..

## Slide 3: TRANsfer reSISTOR
npn BJT or n-channel MOSFET in AC voltage amplifier
+
DC bias current
+
Vin
DC Voltage
Source 1 (Vbias)
Load
DC Voltage
Source 2
Emitter in BJT
Source in FET
Collector in BJT
Drain in FET
Base in BJT
Gate in FET

## Slide 4: TRANSISTOR
+
DC bias current
+
Vin
DC Voltage
Source 1 (Vbias)
Load
DC Voltage
Source 2
Emitter in BJT
Source in FET
Collector in BJT
Drain in FET
Base in BJT
Gate in FET
in AC voltage amplifier

## Slide 5: TRANSISTOR
in AC voltage amplifier
+
DC bias current
+
Vin
DC Voltage
Source 1 (Vbias)
Load
DC Voltage
Source 2
Emitter in BJT
Source in FET
Collector in BJT
Drain in FET
Base in BJT
Gate in FET
Vcc in BJT circuits
Vdd in MOSFET
circuits

## Slide 6: (n-channel) MOSFET current -voltage characteristics
+
VDS
+
VGS
A
depth
DC drain current
DC Gate-to-source voltage > Threshold voltage Vtn
we adopt Vtn = +0.7V for n –channel MOSFET fabricated with 0.5 um technology
VGS = + 1V => overdrive voltage Vov = 0.3 V

## Slide 7: Testing MOSFET
ID
Let us use two separate power supplies : gate-source and drain-source voltage sources
We will keep VGS constant at a certain value above threshold: VGS =1 V
and will measure drain current ID as a function of drain-source voltage VDS

## Slide 8: MOSFET output characteristic
The drain current is almost constant for VDS > Vov =VGS-Vtn
VGs =const = 1 V
(it means Vov = const =0.3 V)

## Slide 9: Output characteristic
You have to keep all MOSFETs in the saturation region under any conditions
(otherwise you get a resistor of inferior quality)
Saturation region
Linear
region
V_DS > V_ov

## Slide 10: Family of output characteristics
Keep MOSFET in the saturation region all the time!
Vov2= 0.2 V
=0.3V
Vov3=0.4V
Vov1= 0.1 V
V_DS > V_ov

## Slide 11: Transfer characteristic
VDS = const
Design parameter: Overdrive voltage Vov = VGS-Vtn
+
VDS
+
VGS
A
DC drain current
in the saturation region
Varied with Vgs
VGS varied => overdrive voltage Vov varied
Keep the MOSFET in the saturation region: VDS > Vov

## Slide 12: Transfer characteristic
VDS = const
Overdrive voltage Vov = VGS-Vtn
is a design parameter
IDsat
VGS
DC drain current
in the saturation region
Varied with Vgs
Keep the MOSFET in the saturation region: VDS > Vov

## Slide 13: (n-channel) MOSFET drain current in the saturation region

## Slide 14: p-channel MOSFETs

## Slide 15: Typical process parameters for a 0.5 µm node technology
The process transconductance parameters for n-MOSFET and p-MOSFET:
Mobility of electrons is approximately a factor of 3 greater than that for holes

## Slide 16: Design parameters
To obtain the required current you have control on 3 design parameters: W, L, Vov
MOSFET represents a voltage-controlled current source (given VDS > Vov)

## Slide 17: Design parameters: Vov, W, L
Example:

## Slide 18: Symbols for enhancement–mode MOSFETs
Equivalent symbols for the n-channel devices
The source terminal at the bottom, it has
negative potential compared to the gate
and drain potentials. Connection of the body
terminal to –Vss is assumed for the lower level symbols.
Equivalent symbols for p-channel devices.
In circuit diagrams p-MOSFETs appears
up-side down with the source terminal on the top because it has higher potential compared to the gate and drain potentials