Module 1
Intrinsic semiconductors: pure element
Extrinsic (doped) semiconductors: added impurities to increase current
 - Donor impurities like phosphorus produce N-type semiconductors
 - Acceptor impurities like boron produce P-type semiconductors
Electrons move by drift and diffusion

---
Biased Clipper Circuits
- Clips signals

---
Biased Clipper Circuit

---
Biased Clamper Circuit
- Shifts signals

---
Biased Clamper Circuit
- Shifts signals
(a) shifts signal waveform up to 0v min
(b) shifts signal waveform up to -5v min
(c) shifts signal waveform down to +5v max
Remember to account for Vf.

---
Diode parameters
- PIV – Peak inverse (reverse) voltage
- Reverse biased diodes are treated as open
- Forward biased diodes are treated as shorts and a voltage source

---
Rectifier Circuits
Center tapped formulae
 - v S (max) = v O (max) + Vγ
 - PIV = v R (max) = 2v S (max) − Vγ
Bridge rectifier formulae
 - v S (max) = v O (max) + 2Vγ
 - PIV = v R (max) = v S (max) − Vγ